## Slide 1: Data Acquisition.
Week 3, Lecture 1
Digital Forensic | ICT312

## Slide 2: Today's Agenda
Understanding Storage Formats for Digital Evidence
Determining the Best Acquisition Method
Contingency Planning for Image Acquisitions
Using Acquisition Tools
Validating Data Acquisitions
Performing RAID Data Acquisitions
Using Remote Network Acquisition Tools
Using Other Forensics Acquisition Tools

## Slide 3: Understanding Storage Formats for Digital Evidence
Proprietary Formats in Digital Forensics
Proprietary formats in digital forensics offer specialized features that integrate with vendor analysis tools.
Key features include:
- Compression options for image files (saving space on target drives)
- Segmented file creation for archiving (CDs/DVDs) with data integrity checks
- Metadata integration (acquisition time, hash values, investigator details, case comments)
Challenges include:
- Incompatibility between vendors' tools (e.g., ILookIX formats readable only by ILook,IX)
- File size limitations (typically 650 MB segments, max 2 GB due to FAT constraints)
- Expert Witness Compression format as an unofficial standard (used by EnCase, supported by multiple tools)

## Slide 4: Understanding Storage Formats for Digital Evidence
Advanced Forensic Format
Dr. Simson L. Garfinkel developed the open-source Advanced Forensic Format (AFF).
AFF is an open-source data acquisition format that stores image data and metadata.
File extensions include .afd for segmented image files and .afm for AFF metadata.
Design goals of AFF:
Capable of producing compressed or uncompressed image files
No size restriction for disk-to-image files
Space in the image file or segmented files for metadata
Simple design with extensibility
Open source for multiple computing platforms and OSs
Internal consistency checks for self-authentication
Digital forensics vendors have no implementation restrictions on this format due to its open-source nature.
For more information, see www.afflib.sourceforge.net and www.basistech.com/wp-content/uploads/datasheets/Digital-Forensics-Toolsets-EN.pdf.

## Slide 5: Knowledge Check: Understanding Storage Formats for Digital Evidence
Which of the following statements accurately describes the Advanced Forensic Format (AFF)?
  A) It is a proprietary format exclusively used by one vendor.
  B) It is an open-source format that is gaining recognition among forensic examiners.
  C) It is a deprecated format no longer supported by any forensic tools.
  D) It is a format that only supports read-only access to digital evidence.
Answer: B - The Advanced Forensic Format (AFF) is an open-source format that is gaining recognition from some forensic examiners, as mentioned in the text.
Let's Apply This!

## Slide 6: Determining the Best Acquisition Method
Static Acquisition: Used when a suspect drive is write-protected and cannot be altered. It is repeatable and preferred for digital evidence collection.
Live Acquisition: Used when the suspect computer cannot be shut down. Captured data may be altered as the OS continuously changes data, making it non-repeatable.
Static acquisition is preferred for seized computers during police raids. Live acquisition is used when the computer is powered on and logged in by the suspect.
Static acquisition is preferred for digital evidence, but has limitations with encrypted drives or network-accessible computers.
Solutions like Elcomsoft Forensic Disk Decryptor can help decrypt encrypted drives.

## Slide 7: Determining the Best Acquisition Method
Disk-to-image file: Most common method, creates bit-for-bit copies, allows flexibility for analysis. Can be read by commercial forensics tools. GUI programs save time and resources.
Disk-to-disk copy: Used when creating disk-to-image files is not feasible, especially with older drives. Adjusts target disk geometry to match original drive. Tools include EnCase and X-Ways Forensics.
Logical acquisition: Captures specific files of interest (e.g., Outlook .pst files) or specific records from large systems. Preferred for large data storage systems and e-discovery.
Sparse acquisition: Captures specific files and fragments of unallocated data. Used when examining the entire drive is not necessary. Example: e-mail investigations requiring only specific file types.
Considerations: Size of source disk, ability to retain source disk, time constraints, and location of evidence. Use lossless compression to reduce target drive size when possible.
Hash verification: Perform MD5 or SHA-1 hashes before and after compression to ensure data integrity. Use multiple algorithms for added reliability.

## Slide 8: Knowledge Check: Determining the Best Acquisition Method
Which acquisition method is most appropriate when you need to collect only specific files (e.g., Outlook .pst files) and do not require examining the entire drive?
  A) Disk-to-image file
  B) Disk-to-disk copy
  C) Logical acquisition
  D) Sparse acquisition
Answer: C - Logical acquisition is designed to capture only specific files of interest, such as Outlook .pst files, without copying the entire drive. This method is efficient for large drives where only certain data is needed.
Let's Apply This!

## Slide 9: Contingency Planning for Image Acquisitions
Create at least two images of digital evidence to minimize risk of failure.
Use different imaging tools (e.g., FTK Imager Lite and X-Ways Forensics) for cross-verification of data integrity.
For critical investigations, duplicate images using the same tool but with different compression settings.
Verify if acquisition tools can access the host protected area (HPA) of a disk drive.
Use hardware tools with write-blockers (e.g., Image MASSter Solo) for HPA access.
Prepare for encrypted drives by understanding decryption processes and tools like Elcomsoft Forensic Disk Decryptor.
Be aware of challenges with decryption keys in criminal investigations where suspects may withhold cooperation.
Consider RAM-based password recovery techniques for encrypted data (e.g., Princeton University research).

## Slide 10: Knowledge Check: Contingency Planning for Image Acquisitions
Which of the following is a recommended contingency planning strategy for ensuring the integrity of digital evidence during image acquisitions?
  A) Using a single imaging tool for all acquisitions to streamline the process.
  B) Creating only one image of the disk to save time and resources.
  C) Making at least two images of the digital evidence, using different tools if possible.
  D) Ignoring the host protected area (HPA) since it's not accessible through standard tools.
Answer: C - The text emphasizes the importance of creating at least two images of digital evidence to minimize the risk of failure. Using different tools can help ensure data is copied correctly, as different tools may handle corrupted areas differently.
Let's Apply This!

## Slide 11: Using Acquisition Tools
Mini-WinFE Boot CDs and USB Drives
Mini-WinFE is a forensic boot utility that enables building a Windows forensic boot CD/DVD or USB drive.
It allows connected drives to be mounted as read-only for forensic acquisition.
Use case: When direct disk access is impractical (e.g., laptop design, lack of appropriate connectors).
Provides a way to write-protect the disk drive during acquisition.
Supports both Windows and Linux-based forensic boot options.

## Slide 12: Acquiring Data with a Linux Boot CD
Using Linux Live CD Distributions
Linux Live CDs (e.g., Ubuntu, openSUSE, Arch Linux, Fedora, Slackware) provide ISO images for booting without installation.
Most distributions are for OS recovery, not digital forensics. See livecdlist.com for current lists.
Specialized forensic distributions include: Penguin Sleuth Kit, CAINE, Deft, Kali Linux, Knoppix, SIFT.
These tools include forensic utilities and prevent media mounting to preserve data integrity.
Acquire ISOs on any OS (Windows), burn to CD/DVD with tools like Nero/Roxio, or use USB drives with ISO-to-USB tools.

## Slide 13: Acquiring Data with a Linux Boot CD
Preparing a Target Drive for Acquisition in Linux
Linux supports modifying non-Linux file systems including FAT and NTFS
Linux can create Microsoft FAT and NTFS partition tables
Kernel versions 2.6.17.7 and earlier support FAT read-only with NTFS-3G driver for write access
NTFS-3G driver available at http://sourceforge.net/projects/ntfs-3g
For macOS file systems, refer to Chapter 7

## Slide 14: Acquiring Data with a Linux Boot CD
Preparing a Target Drive for Acquisition in Linux
Boot Linux on your computer (Live CD or installed system).
Connect the external drive (USB, FireWire, SATA) and power it on.
Open a shell prompt; use 'su' to switch to root (if not already in root).
List disk devices with 'fdisk -l' to identify the target drive (e.g., /dev/sda).
Use 'fdisk /dev/sda' to create a FAT32 partition:
- Type 'n' to create a new partition (default selects entire drive).
- Type 't' to change partition type to FAT32 (code 'c').
- Type 'w' to write changes and exit fdisk.
Format the partition with 'mkfs.msdos -vF32 /dev/sda1' (install dosfstools if needed).
Close shell session; the drive is now ready for image acquisition.

## Slide 15: Acquiring Data with a Linux Boot CD
Preparing a Target Drive for Acquisition in Linux
Boot Linux on your computer and connect the external drive.
Open a shell prompt and use 'su' to switch to root (if not already in root mode).
List disk devices with 'fdisk -l' to identify the target drive (e.g., /dev/sda).
Use 'fdisk /dev/sda' to create a new primary FAT32 partition:
- Type 'n' to create a new partition.
- Select 'p' for primary and '1' for the first partition.
- Confirm defaults to use the entire drive.
- Type 't' to change the partition type to FAT32 (code 'c').
- Save changes with 'w' to write the partition table.
Format the partition with 'mkfs.msdos -vF32 /dev/sda1' to create a FAT32 file system.
Close the shell session and mount the drive for use in acquisition.

## Slide 16: Acquiring Data with a Linux Boot CD
Preparing a Target Drive for Acquisition in Linux
Use mkfs.msdos -vF32 /dev/sda1 to format the FAT file system.
If mkfs.msdos is missing, install dosfstools package (e.g., search for 'mkfs.msdos Fedora' or 'dostools Debian').
Newer Linux distributions automatically sync the partition, eliminating the need for reboot.
Close the shell session with 'exit' to mount and use the FAT target drive for image acquisition.

## Slide 17: Acquiring Data with a Linux Boot CD
Acquiring Data with dd in Linux
A forensics Linux Live CD can mount and read most drives.
Required tools: USB/FireWire/SATA external drive, knowledge of BIOS settings, and shell commands.
The dd command is used for data acquisition, creating raw format files for forensic analysis.
dd can copy entire devices including unallocated space, without requiring the drive to be mounted.
Caution: Misuse of dd can lead to data destruction on the original drive.

## Slide 18: Acquiring Data with a Linux Boot CD
Acquiring Data with dd in Linux
The dd command is used for copying data between devices or files in Linux.
It can read and write data from a media device to a data file.
dd is not bound by a logical file system's data structures, allowing access to unmounted drives.
It copies entire devices, including data files, slack space, and unallocated data.
The output is in raw format, suitable for forensic analysis tools.

## Slide 19: Acquiring Data with a Linux Boot CD
Acquiring Data with dd in Linux
Use caution with dd command to avoid data overwrite
Ensure correct identification of suspect and target drives
Segment large drives using split command with -b switch
Create segmented volumes suitable for FAT32 (<=2GB per segment)
Use numeric extensions for Windows forensics tools (e.g., image_sdb.01)
For specific partitions, use /dev/sdb1 format with dd command
Verify drive mounting with fdisk -l before data acquisition
Create mount points and directories for target drives
Unmount target drive after acquisition with umount command
Consider alternative storage solutions for large drives

## Slide 20: Acquiring Data with a Linux Boot CD
Acquiring Data with dcfldd in Linux
The dd command is not designed for forensic acquisitions but serves as a data management tool.
dcfldd was developed by Nicholas Harbour of DCFL to address forensic needs in UNIX/Linux systems.
dcfldd offers enhanced features for forensic acquisitions compared to dd, including:
- Specifying hexadecimal patterns or text for clearing disk space
- Logging errors to an output file for analysis
- Hashing options (MD5, SHA-1, SHA-256, SHA-384, SHA-512) with logging and byte-specific hashing
- Status display for acquisition progress in bytes
- Segmented volumes with numeric extensions (beyond dd's 99 limit)
- Data verification with the original disk/media
- Caution: dcfldd can also write to the wrong device if not used carefully

## Slide 21: Using Acquisition Tools
Capturing an Image with AccessData FTK Imager Lite
Document the chain of evidence for the drive you plan to acquire.
Remove the drive from the suspect’s computer.
For IDE drives, configure the suspect drive’s jumpers as needed (SATA/USB drives do not require this step).
Connect the suspect drive to the USB or FireWire write-blocker device.
Create a storage folder on the target drive (e.g., C:\Work\Chap03\Chapter for this activity).

## Slide 22: Using Acquisition Tools
Capturing an Image with AccessData FTK Imager Lite
FTK Imager is a data acquisition tool included with a licensed copy of AccessData Forensic Toolkit.
It requires a USB dongle for licensing, except for FTK Imager Lite, Debian/Ubuntu x64, and macOS 10.5/10.6x command-line interfaces which are free and dongle-free.
Supports reading various formats: .ad1, .e01, .s01, AFF, raw, CD/DVD file systems.
Can create disk-to-image copies at physical or logical partition levels.
Allows segmentation into split volumes (e.g., 650 MB for CDs, 2.0 GB for DVDs).
Can image RAM on a live computer using a Live CD like Mini-WinFE.
Cannot acquire HPA and DCO areas; requires advanced tools for these regions.

## Slide 23: Using Acquisition Tools
Capturing an Image with AccessData FTK Imager Lite
Boot forensic workstation to Windows using an installed write-blocker.
Connect evidence drive to write-blocking device or USB device.
Connect target drive to USB external drive if using a write-blocker.
Launch FTK Imager Lite and accept User Account Control prompt.
Navigate to File > Create Disk Image to initiate the process.
Select Physical Drive as source and choose the suspect drive.
Configure image settings: Verify images, select Raw (dd) format.
Enter case information in Evidence Item Information dialog.
Specify image destination folder (e.g., C:\Work\Chap03\Chapter).
Set image fragment size to default 1500 MB or adjust as needed.
Name the image file (e.g., InChp03-ftk) and click Finish.
Start the acquisition process and review verification results.
Close all dialogs and exit FTK Imager Lite after completion.

## Slide 24: Using Acquisition Tools
Capturing an Image with AccessData FTK Imager Lite
Boot forensic workstation to Windows using installed write-blocker.
Connect evidence drive to write-blocking device or USB device.
Connect target drive to USB external drive if using write-blocker.
Launch FTK Imager Lite and accept User Account Control prompt.
Select File > Create Disk Image to initiate the process.
Choose Physical Drive option and select the suspect drive.
Verify images after creation and select Raw (dd) image type.
Complete case information in Evidence Item Information dialog.
Specify image destination folder (e.g., Work\Chap03\Chapter) and ensure AD Encryption is unchecked.
Set image filename as InChp03-ftk and click Finish.
Start acquisition and review verification results upon completion.
Exit FTK Imager Lite after image creation.

## Slide 25: Knowledge Check: Using Acquisition Tools
Which of the following is a correct statement about using acquisition tools for digital forensics?
  A) All modern acquisition tools can reliably acquire data from a disk's HPA.
  B) Write-blocking hardware is always required when acquiring data from a suspect drive in Windows or Linux.
  C) Using USB-3 devices is not recommended due to potential data corruption risks.
  D) Some countries have fully accepted the use of write-blocking devices for data acquisitions without legal concerns.
Answer: B - Write-blocking hardware is essential to prevent data contamination when acquiring evidence from a suspect drive in Windows or Linux, as these OSs can automatically mount and modify the drive.
Let's Apply This!

## Slide 26: Linux Validation Methods
Validating dd-Acquired Data
Use md5sum to validate segmented volumes of a suspect drive
Navigate to the directory containing saved image files
Calculate hash value of original drive: `md5sum /dev/sdb > md5_sdb.txt`
Compute MD5 hash for segmented volumes: `cat image_sdb.* | md5sum >> md5_sdb.txt`
Concatenate all segmented volumes as a single contiguous file
Pipe data to md5sum for hash calculation
Append results to md5_sdb.txt for comparison

## Slide 27: Linux Validation Methods
Validating dd-Acquired Data
Calculate hash value of original drive: `md5sum /dev/sdb > md5_sdb.txt`
Compute MD5 hash for segmented volumes: `cat image_sdb.* | md5sum >> md5_sdb.txt`
Verify hashes match: `cat md5_sdb.txt`
If hashes match, acquisition is successful; otherwise, data acquisition failed
Use `sha1sum` instead of `md5sum` by replacing all references
Ensure drive remains connected during validation
Save md5_sdb.txt with image files for validation

## Slide 28: Linux Validation Methods
Validating dcfldd-Acquired Data
dcfldd integrates validation options for forensic data acquisition: hash and hashlog.
Hash options: md5, sha1, sha256, sha384, sha512.
Hashlog outputs hash results to a text file stored with image files.
Example command for MD5 hash output during acquisition: dcfldd if=/dev/sda of=image.dd hash=md5 hashlog=hashlog.txt

## Slide 29: Validating Data Acquisitions
Windows Validation Methods
Windows lacks built-in hashing tools for digital forensics, relying on third-party programs.
Third-party tools include hexadecimal editors (e.g., X-Ways WinHex, Hex Workshop) and forensics software (e.g., OSForensics, Autopsy, EnCase, FTK).
Commercial tools have proprietary validation techniques for acquisition data formats.
Autopsy uses MD5 to validate images by reading metadata from Expert Witness Compression or AFF files.
Raw format images lack metadata, requiring manual validation for integrity checks.
FTK Imager Lite provides validation reports with MD5 and SHA-1 hashes for .e01 and .s01 formats.
Open-source tools like md5deep and Hash-Tool are available for Windows hashing.

## Slide 30: Knowledge Check: Validating Data Acquisitions
Which of the following statements accurately describes the role of hashing algorithms in validating data acquisitions?
  A) They are used to create a unique digital fingerprint that represents the data's integrity.
  B) They are primarily used to compress data for faster transfer.
  C) They are used to encrypt data to prevent unauthorized access.
  D) They are used to delete data permanently from storage devices.
Answer: A - Hashing algorithms generate a unique digital fingerprint (hash value) that represents the data's integrity. Any alteration in the data, even a minor one, results in a completely different hash value, making it a critical tool for validating data acquisitions.
Let's Apply This!

## Slide 31: Performing RAID Data Acquisitions
Understanding RAID
RAID (Redundant Array of Independent Disks) is a computer configuration using two or more physical disks.
RAID configurations serve multiple purposes: data redundancy for fault tolerance, and data striping for improved access speeds.
RAID can be implemented through software (Software RAID) or hardware controllers (Hardware RAID).
Software RAID is managed by the host OS, while Hardware RAID uses dedicated controllers with their own processors and memory.
RAID levels include 0, 1, 5, 6, 10, and 15, each with distinct characteristics and use cases.
RAID 0 (Striping): Combines multiple disks into a single volume for increased speed and storage capacity, but lacks redundancy.
RAID 1 (Mirroring): Uses two identical disks for redundancy, ensuring data availability if one disk fails.
RAID 5 (Distributed Parity): Combines striping with distributed parity across all disks, enabling data recovery from single disk failures.
RAID 6 (Double Parity): Enhances RAID 5 with double parity, allowing recovery from two disk failures.
RAID 10 (Mirrored Striping): Combines RAID 1 and RAID 0 for both redundancy and performance.
RAID 15 (Mirrored Striping with Parity): Combines RAID 1 and RAID 5 for robust data recovery and high performance, but at higher cost.

## Slide 32: Performing RAID Data Acquisitions
Acquiring RAID Disks
Assess data storage requirements for a complete forensics image
Identify RAID type: Windows RAID (0, 1) or hardware-firmware RAID (5, 10, 15) or unknown configuration
Determine if all drives must be connected for the OS to read data (especially for RAID 1, 10, 15 systems)
Verify tool capability to copy data accurately and read forensic RAID images
Check if the tool can handle split data saves and combine RAID disk images into a virtual drive
Consider using compressed proprietary formats to reduce storage needs for large RAID systems
Use large-capacity drives (e.g., 300 GB SATA/IDE) for copying small RAID systems
Leverage RAID recovery features in forensic tools like EnCase, X-Ways Forenssics, and FTK

## Slide 33: Knowledge Check: Performing RAID Data Acquisitions
Which of the following is the primary challenge in acquiring data from RAID systems, as highlighted in the text?
  A) The complexity of RAID configuration and management
  B) The need for specialized forensic tools
  C) The size of RAID systems, often reaching exabytes
  D) The risk of data corruption during acquisition
Answer: C - The text explicitly states that size is the biggest concern in RAID data acquisitions, as many RAID systems are now pushing into exabytes or more of data.
Let's Apply This!

## Slide 34: Using Remote Network Acquisition Tools
Remote Acquisition with ProDiscover
Capture volatile system state information
Analyze current running processes on a remote system
Locate unseen files and processes on a remote system that might be running malware or spyware
Remotely view and listen to IP ports on a compromised system
Run hash comparisons on a remote system to search for known Trojans and rootkits
Create a hash inventory of all files on a system remotely (negative hash search capability) to establish a baseline if it gets attacked

## Slide 35: Using Remote Network Acquisition Tools
Remote Acquisition with ProDiscover
PDServer Remote Agent Installation Methods:
1. Trusted CD: ProDiscover creates a special CD/DVD or USB drive with PDServer for manual installation on the suspect computer.
2. Preinstallation: PDServer is added to the standard installation of high-risk computers in configured networks, enabling quick response to attacks. Tools like DameWare or Hyena can initiate connections.
3. Pushing out and running remotely: PDServer is downloaded to a remote computer, allowing real-time data collection during incident response.
Security Features:
• Stealth Mode: PDServer can be disguised as an OS function (e.g., renamed process) to hide from the suspect.
• Password Protection: PDServer is password-protected with encrypted passwords.
• Encryption: 256-bit AES or Twofish encryption secures communication between systems.
• Secure Communication Protocol: GUIDs prevent packet insertion in data streams.
• Write-Protected Trusted Binaries: PDServer runs from write-protected devices like CDs.
• Digital Signatures: PDServer and PARemoval.sys are digitally signed to ensure integrity.

## Slide 36: Using Remote Network Acquisition Tools
Remote Acquisition with EnCase Enterprise
Guidance Software pioneered remote acquisition with EnCase Endpoint Investigator, an extension of its desktop tool EnCase.
Key Features:
Search and collect internal and external network systems across wide geographical areas
Support for multiple operating systems and file systems
Triage capabilities to assess system relevance to an investigation
Simultaneous search of up to five systems
For more information: www.guidancesoftware.com/docs/default-source/document-library/product-brief/encase-endpoint-investigator-product-overview.pdf

## Slide 37: Knowledge Check: Using Remote Network Acquisition Tools
Which of the following is a significant drawback of using remote network acquisition tools in digital forensics?
  A) The requirement for advanced privileges to push agent applications to the remote system
  B) The necessity to manually intervene on the suspect's computer to initiate data copy
  C) The potential for antivirus and firewall tools to block remote access programs
  D) The inability to perform live acquisitions without physical access to the suspect's computer
Answer: C - Antivirus and firewall tools can block remote access programs, and suspects with administrator rights may install their own security tools that trigger alerts, making remote acquisition more challenging.
Let's Apply This!

## Slide 38: Using Other Forensics Acquisition Tools
ASR Data SMART
Creates image files of suspect drives
Supports proprietary or raw format images
Robust data reading of bad sectors
Mounts suspect drives in write-protected mode
Mounts target drives (including NTFS) in read/write mode
Optional compression schemes for faster acquisition or storage reduction

## Slide 39: Using Other Forensics Acquisition Tools
Runtime Software
Runtime Software and R-Tools Technologies are data recovery tools designed for RAID data recovery and forensics acquisition.
Key Features:
- RAID Reconstructor: Copies RAID to raw format file for restoration on another RAID system; scans and corrects errors on the copied RAID.
- R-Studio: Creates a virtual volume of RAID image file for repairs, which can then be restored to original RAID.
- Supports RAID 0, RAID 5, and other RAID configurations.
- Enables raw format acquisitions and repairs for broken RAID systems.
- Allows segmentation of raw or compressed images for archiving.
- Offers file system-specific tools (FAT/NTFS) for data acquisition.
- Can access network drives for data recovery.
- Provides compressed acquisition options to reduce target drive size requirements.

## Slide 40: Knowledge Check: Using Other Forensics Acquisition Tools
Which of the following statements accurately reflects information from the provided text about commercial forensics acquisition tools?
  A) All commercial tools are equally priced for everyone.
  B) Law enforcement officers working in digital forensics can get discounted prices for some tools.
  C) The text only discusses open-source tools and not commercial ones.
  D) There are no discounts available for any commercial forensics tools.
Answer: B - The text explicitly mentions that prices for some tools are discounted for law enforcement officers working in digital forensics, making option B the correct answer.
Let's Apply This!

## Slide 41: Summary & Key Takeaways
Digital forensics requires precise acquisition methods, including tools like FTK, EnCase, and ProDiscover for capturing volatile data and creating secure, hash-integrity images.
RAID systems demand specialized handling, with tools like Runtime Software and R-Tools enabling reconstruction, segmentation, and virtual volume creation for forensic analysis.
Remote acquisition tools face challenges like antivirus/firewall interference but offer critical capabilities for incident response and live system analysis through secure protocols.
Commercial tools often provide discounts for law enforcement, and open-source alternatives like ASR Data SMART offer flexibility for RAID recovery and data acquisition.
Effective forensics workflows balance speed, security, and scalability, leveraging both local and remote acquisition strategies to meet investigative needs.

## Slide 42: Questions?